## Slide 1: Chapter 1: Introduction CSCI 410 Operating Systems

## Slide 2: Chapter 1: Introduction to Course
What Operating Systems Do
Computer-System Organization
Computer-System Architecture
Operating-System Structure
Operating-System Operations
Process Management
Memory Management
Storage Management
Protection and Security
Distributed Systems
Special-Purpose Systems
Computing Environments
Open-Source Operating Systems

## Slide 3: Chapter Objectives
To provide a grand tour of the major operating systems components
  Chapter 1 is broad coverage but shallow
To provide coverage of basic computer system organization

## Slide 4: What is an Operating System?
A program that acts as an intermediary between a user of a computer and the computer hardware
Operating system goals:
  Execute user programs (Safely!)
  Make the computer system convenient to use
  Use the computer hardware in an efficient manner

## Slide 5: Computer System Structure
Computer system can be divided into four components:
  Hardware – provides basic computing resources
    CPU, memory, I/O devices
  Operating system
    Controls and coordinates use of hardware among various applications and users
  Application programs – Software to solve computing problems of users
    Word processors, compilers, web browsers, database systems, video games
  Users
    People, machines, other computers

## Slide 6: Four Components of a Computer System

## Slide 7: What Operating Systems Do
Depends on point of view
Users want convenience, ease of use
  Don’t care about resource utilization
Shared computers such as mainframe or minicomputer must keep all users happy
Users of dedicate systems such as workstations have dedicated resources
  Still share among processes
Handheld computers are resource poor, optimized for usability and battery life
Some computers have little or no user interface, such as embedded computers in devices and automobiles

## Slide 8: Operating System Definition
OS is a resource allocator
  Manages all resources
  Decides between conflicting requests for efficient and fair resource use
OS is a control program
  Controls execution of programs to prevent errors and improper use of the computer

## Slide 9: Operating System Definition (Cont.)
No universally accepted definition
“Everything a vendor ships when you order an operating system” is good approximation
  But varies wildly
“The one program running at all times on the computer” is the kernel. Everything else is either a system program (ships with the operating system) or an application program.

## Slide 10: Computer Startup
bootstrap program is loaded at power-up or reboot
  Typically stored in ROM or EPROM, generally known as firmware
  Initializes all aspects of system
  Loads operating system kernel and starts execution

## Slide 11: Computer System Organization
Computer-system operation
  One or more CPUs, device controllers connect through common bus providing access to shared memory
  Concurrent execution of CPUs and devices competing for memory cycles

## Slide 12: Computer-System Operation
I/O devices and the CPU can execute concurrently
Each device controller is in charge of a particular device type
Each device controller has a local buffer (RAM)
CPU moves data from/to main memory to/from local buffers
I/O is from the device to local buffer of a controller
Device controller informs CPU that it has finished its operation by causing an interrupt

## Slide 13: Common Functions of Interrupts
Interrupt transfers control to the interrupt service routine generally, through the interrupt vector, which contains the addresses of all the service routines
Interrupt architecture must save the address of the interrupted instruction
Incoming interrupts are disabled while another interrupt is being processed to prevent a lost interrupt
A trap is a software-generated interrupt caused either by an error or a user request
An operating system is interrupt driven

## Slide 14: Interrupt Handling
The operating system preserves the state of the CPU by storing registers and the program counter
Determines which type of interrupt has occurred:
  polling
  vectored interrupt system
Separate segments of code determine what action should be taken for each type of interrupt

## Slide 15: Interrupt Timeline

## Slide 16: I/O Structure Types
After I/O starts, control returns to user program only upon I/O completion
  Wait instruction idles the CPU until the next interrupt
  Wait loop (contention for memory access)
  At most one I/O request is outstanding at a time, no simultaneous I/O processing
After I/O starts, control returns to user program without waiting for I/O completion
  System call – request to the operating system to allow user to wait for I/O completion
  Device-status table contains entry for each I/O device indicating its type, address, and state
  Operating system indexes into I/O device table to determine device status and to modify table entry to include interrupt

## Slide 17: Direct Memory Access Structure
Used for high-speed I/O devices able to transmit information at close to memory speeds
Device controller transfers blocks of data from buffer storage directly to main memory without CPU intervention
Only one interrupt is generated per block, rather than the one interrupt per byte

## Slide 18: Notation Review
Computer storage, along with most computer throughput, is generally measured and manipulated in bytes and collections of bytes.
  bit is a 0/1; byte is 8 bits (nibble is 4 bits!)
  Word depends on CPU register size (native data unit size)
    16 bit, 32 bit, 64, bit
  kilobyte, or KB, is 1,024 bytes
  megabyte, or MB, is 1,0242 bytes
  gigabyte, or GB, is 1,0243 bytes
  terabyte, or TB, is 1,0244 bytes
  petabyte, or PB, is 1,0245 bytes
  exabyte, EB, is 1,0246 bytes (zeta, yota, xenotta, Shilentno, domegemegrotte) (Internet traffic will reach 1.3 ZB in 2016)
NOTE: Network throughput is usually measured in powers of 10.
  10mbps is 10,000,000 bits per second

## Slide 19: Storage Structure
Main memory – only large storage media that the CPU can access directly
  Random access
  Typically volatile
Secondary storage – extension of main memory that provides large nonvolatile storage capacity
Hard disks – rigid metal or glass platters covered with magnetic recording material
  Disk surface is logically divided into tracks, which are subdivided into sectors
  The disk controller determines the logical interaction between the device and the computer
Solid-state disks – faster than hard disks, nonvolatile
  Various technologies
  Becoming more popular

## Slide 20: Storage Hierarchy
Storage systems organized in hierarchy
  Speed
  Cost
  Volatility
Caching – copying information into faster storage system; main memory can be viewed as a cache for secondary storage

## Slide 21: Storage-Device Hierarchy

## Slide 22: Sample Speeds
Writes are expensive!
  Datastore is transactional: writes require disk access
  Disk access means disk seeks
  Rule of thumb: 10ms for a disk seek
  Simple math: 1s / 10ms = 100 seeks/sec maximum
Reads are cheap!
  Reads do not need to be transactional, just consistent
  Data is read from disk once, then it's easily cached
  All subsequent reads come straight from memory
  Rule of thumb: 250usec for 1MB of data from memory
  Simple math: 1s / 250usec = 4GB/sec maximum * For a 1MB entity, that's 4000 fetches/sec

## Slide 23: Sample Speeds
L1 cache reference 0.5 ns
Branch mispredict 5 ns
L2 cache reference 7 ns
Mutex lock/unlock 100 ns
Main memory reference 100 ns
Compress 1K bytes with Zippy 10,000 ns
Send 2K bytes over 1 Gbps network 20,000 ns
Read 1 MB sequentially from memory 250,000 ns
Round trip within same datacenter 500,000 ns
Disk seek 10,000,000 ns
Read 1 MB sequentially from network 10,000,000 ns
Read 1 MB sequentially from disk 30,000,000 ns
Send packet CA->Netherlands->CA 150,000,000 ns

## Slide 24: Caching
Important principle, performed at many levels in a computer (in hardware, operating system, software)
Data in use copied from slower to faster storage temporarily
Faster storage (cache) checked first to determine if data is there
  If it is, data used directly from the cache (fast)
  If not, data copied to cache and used there
Cache smaller than storage being cached
  Cache management important design problem
  Cache size and replacement policy

## Slide 25: Computer-System Architecture
In the past systems used a single general-purpose (GP) processor
  Most systems have special-purpose processors as well
  Today many (most?) have multiple GP cores/processors
Multiprocessor systems becoming common
  Also known as parallel systems, tightly-coupled systems
  Advantages include:
    Increased throughput
    Economy of scale
    Increased reliability – graceful degradation or fault tolerance
  Two types:
    Asymmetric Multiprocessing
    Symmetric Multiprocessing

## Slide 26: How a Modern Computer Works
A von Neumann architecture

## Slide 27: Symmetric Multiprocessing Architecture

## Slide 28: A Dual-Core Design

## Slide 29: Clustered Systems
Like multiprocessor systems, but multiple systems working together
  Usually sharing storage via a storage-area network (SAN)
  Provides a high-availability service which survives failures
    Asymmetric clustering has one machine in hot-standby mode
    Symmetric clustering has multiple nodes running applications, monitoring each other
  Some clusters are for high-performance computing (HPC)
    Applications must be written to use parallelization

## Slide 30: Clustered Systems

## Slide 31: Operating System Structure
Multiprogramming needed for efficiency
  Single user cannot keep CPU and I/O devices busy at all times
  Multiprogramming organizes jobs (code and data) so CPU always has one to execute
  A subset of total jobs in system is kept in memory
  One job selected and run via job scheduling
  When it has to wait (for I/O for example), OS switches to another job
Timesharing (multitasking) is logical extension in which CPU switches jobs so frequently that users can interact with each job while it is running, creating interactive computing
  Response time should be < 1 second
  Each user has at least one program executing in memory process
  If several jobs ready to run at the same time  CPU scheduling
  If processes don’t fit in memory, swapping moves them in and out to run
  Virtual memory allows execution of processes not completely in memory

## Slide 32: Memory Layout for Multiprogrammed System

## Slide 33: Operating-System Operations
Interrupt driven by hardware
Software error or request creates exception or trap
  Division by zero, request for operating system service
Other process problems include infinite loop, processes modifying each other or the operating system
Dual-mode operation allows OS to protect itself and other system components
  User mode and kernel mode (AKA: supervisor mode – protected vs real)
  Mode bit provided by hardware
    Provides ability to distinguish when system is running user code or kernel code
    Some instructions designated as privileged, only executable in kernel mode
    System call changes mode to kernel, return from call resets it to user

## Slide 34: Transition from User to Kernel Mode
Timer to prevent infinite loop / process hogging resources
  Set interrupt after specific period
  Operating system decrements counter
  When counter zero generate an interrupt
  Set up before scheduling process to regain control or terminate program that exceeds allotted time

## Slide 35: Process Management
A process is a program in execution. It is a unit of work within the system. Program is a passive entity, process is an active entity.
Process needs resources to accomplish its task
  CPU, memory, I/O, files
  Initialization data
Process termination requires reclaim of any reusable resources
Single-threaded process has one program counter specifying location of next instruction to execute
  Process executes instructions sequentially, one at a time, until completion
Multi-threaded process has one program counter per thread
Typically system has many processes, some user, some operating system running concurrently on one or more CPUs
  Concurrency by multiplexing the CPUs among the processes / threads

## Slide 36: Process Management Activities
Creating and deleting both user and system processes
Suspending and resuming processes
Providing mechanisms for process synchronization
Providing mechanisms for process communication
Providing mechanisms for deadlock handling
The operating system is responsible for the following activities in connection with process management:

## Slide 37: Memory Management
All data in memory before and after processing
All instructions in memory in order to execute
Memory management determines what is in memory when
  Optimizing CPU utilization and computer response to users
Memory management activities
  Keeping track of which parts of memory are currently being used and by whom
  Deciding which processes (or parts thereof) and data to move into and out of memory
  Allocating and deallocating memory space as needed

## Slide 38: Storage Management
OS provides uniform, logical view of information storage
  Abstracts physical properties to logical storage unit - file
  Each medium is controlled by device (i.e., disk drive, tape drive)
    Varying properties include access speed, capacity, data-transfer rate, access method (sequential or random)
File-System management
  Files usually organized into directories
  Access control on most systems to determine who can access what
  OS activities include
    Creating and deleting files and directories
    Primitives to manipulate files and dirs
    Mapping files onto secondary storage
    Backup files onto stable (non-volatile) storage media

## Slide 39: Mass-Storage Management
Usually disks used to store data that does not fit in main memory or data that must be kept for a “long” period of time
Proper management is of central importance
Entire speed of computer operation hinges on disk subsystem and its algorithms
OS activities
  Free-space management
  Storage allocation
  Disk scheduling
Some storage need not be fast
  Tertiary storage includes optical storage, magnetic tape
  Still must be managed – by OS or applications
  Varies between WORM (write-once, read-many-times) and RW (read-write)

## Slide 40: Performance of Various Levels of Storage
Movement between levels of storage hierarchy can be explicit or implicit

## Slide 41: Migration of Integer A from Disk to Register
Multitasking environments must be careful to use most recent value, no matter where it is stored in the storage hierarchy
Multiprocessor environment must provide cache coherency in hardware such that all CPUs have the most recent value in their cache
Distributed environment situation even more complex
  Several copies of a datum can exist
  Various solutions covered in Chapter 17

## Slide 42: Protection and Security
Protection – any mechanism for controlling access of processes or users to resources defined by the OS
Security – defense of the system against internal and external attacks
  Huge range, including denial-of-service, worms, viruses, identity theft, theft of service
Systems generally first distinguish among users, to determine who can do what
  User identities (user IDs, security IDs) include name and associated number, one per user
  User ID then associated with all files, processes of that user to determine access control
  Group identifier (group ID) allows set of users to be defined and controls managed, then also associated with each process, file
  Privilege escalation allows user to change to effective ID with more rights

## Slide 43: Distributed Computing
Collection of separate, possibly heterogeneous, systems networked together
  Network is a communications path
      Local Area Network (LAN)
      Wide Area Network (WAN)
      Metropolitan Area Network (MAN)
Network Operating System provides features between systems across network
  Communication scheme allows systems to exchange messages
  Illusion of a single system

## Slide 44: Special-Purpose Systems
Real-time embedded systems most prevalent form of computers
  Vary considerable, special purpose, limited purpose OS, real-time OS
Multimedia systems
  Streams of data must be delivered according to time restrictions
Handheld systems
  PDAs, smart phones, limited CPU, memory, power
  Reduced feature set OS, limited I/O

## Slide 45: Computing Environments
Traditional computer
  Blurring over time
  Office environment
    PCs connected to a network, terminals attached to mainframe or minicomputers providing batch and timesharing
    Now portals allowing networked and remote systems access to same resources
  Home networks
    Used to be single system, then modems
    Now firewalled, networked

## Slide 46: Computing Environments (Cont.)
Client-Server Computing
  Dumb terminals supplanted by smart PCs
  Many systems now servers, responding to requests generated by clients
    Compute-server provides an interface to client to request services (i.e., database)
    File-server provides interface for clients to store and retrieve files

## Slide 47: Peer-to-Peer Computing
Another model of distributed system
P2P does not distinguish clients and servers
  Instead all nodes are considered peers
  Each may act as client, server or both
  Node must join P2P network
    Registers its service with central lookup service, or
    Broadcast request for service and respond to requests for service via discovery protocol
  Examples include Napster, BitTorrent, and Gnutella

## Slide 48: Virtualization
Allows operating systems to run applications within other OSes
  Vast and growing industry
Emulation used when source CPU type different from target type (i.e. PowerPC to Intel x86)
  Generally slowest method
  When computer language not compiled to native code – Interpretation
Virtualization – OS natively compiled for CPU, running guest OSes also natively compiled
  Consider VMware running WinXP guests, each running applications, all on native WinXP host OS
  VMM (virtual machine Manager) provides virtualization services

## Slide 49: Virtualization

## Slide 50: Web-Based Computing
Web has become ubiquitous
PCs most prevalent devices
More devices becoming networked to allow web access
New category of devices to manage web traffic among similar servers: load balancers
Use of operating systems like Windows 95, client-side, have evolved into Linux and Windows XP, which can be clients and servers

## Slide 51: Cloud Computing
Delivers computing, storage, even apps as a service across a network
Logical extension of virtualization because it uses virtualization as the base for it functionality.
  Amazon EC2 has thousands of servers, millions of virtual machines, petabytes of storage available across the Internet, pay based on usage
Many types
  Public cloud – available via Internet to anyone willing to pay
  Private cloud – run by a company for the company’s own use
  Hybrid cloud – includes both public and private cloud components
  Software as a Service (SaaS) – one or more applications available via the Internet (i.e., word processor)
  Platform as a Service (PaaS) – software stack ready for application use via the Internet (i.e., a database server)
  Infrastructure as a Service (IaaS) – servers or storage available over Internet (i.e., storage available for backup use)

## Slide 52: Cloud Computing

## Slide 53: Open-Source Operating Systems
Operating systems made available in source-code format rather than just binary closed-source
Counter to the copy protection and Digital Rights Management (DRM) movement
Started by Free Software Foundation (FSF), which has “copyleft” GNU Public License (GPL)
Examples include GNU/Linux, Android, and, BSD UNIX (including core of Mac OS X), and many more

## Slide 54: End of Chapter 1 Material Skipped: OS Data Structures (please read this and ask questions if needed.)